## Slide 1: RMS Tuning(Just do it!) and Indexed Files Internals, Patching
Hein van den Heuvel
First presented as session 705, CETS 2000
Updated 2/14/2003
hein@hp.com

## Slide 2: Anatomy of an Indexed File
Areas
Prologue
Key 0
Primary
Key 1
Alternate
2
1
0
Root
6 *
Index
2 6
Index
*
Data
1 2
Data
3 6
Data
7
Root
Smith *
Index
Jones Smith
SIDR
Bell Jones
SID
Sla..
Down
Down key
Down
Down index
Next
Down
Next
Next
ANALYZE/RMS/INT

## Slide 3: Design For Performance
Work with the numbers
    RMS does (unfortunately) no magic
    All RMS activity is rather predictable
    Calculate/predict IO resource needs
    Instrument application
      SYS$GETJPI / LIB$SHOW_TIMER
      SET FILE /STATISTICS followed by
        MONITOR RMS /ITEM=CACH …
        RMS_STATS tool on VMS Freeware CD
    Compare Expected and Actual measurements

## Slide 4: Production Systems
Regular Converts for indexed files
    Daily / Weekly / Monthly / Yearly based on usage
    Combats both Internal and External fragmentation
    Opportunity to tune
    Delivers basic statistics: record count
    Implied backup
    Implied sanity check
      Corruption might not yet show in production

## Slide 5: Production Systems
Periodic Analyze / Optimize
    Index root level(s) still as planned ?
    Bucket size still adequate ?
    Number of (global) buffers still adequate ?
    File size still as planned ?
Standard tools
    $ANALYZE/RMS $MONITOR…
    $EDIT/FDL/NOINTERACTIVE
    $DIRECTORY/FULL

## Slide 6: Performance still bad ?
Is there a bottleneck ?
  CPU : $MONI MODE
      INTERRUPT = Devices and cluster locks
      MPSYNC = Kernel access serialization (locks?)
      KERNEL = Locks and QIO and logical names
      EXECUTIVE = RMS (or ORACLE or…)
      USER = real work!
  IO : $MONI DISK, IO, PROC/TOPDIO
      Watch out for MONI DISK/TOPQ because serial reads will NOT cause a queue and yet still be an IO problem!
  LOCKS: $MONI LOCK, DLOCK

## Slide 7: Performance still bad ?
No IO problem, No CPU problem, and still No Performance? Probably Serialization!
Basic application understanding
    “Master record with ‘next key’ value”
    mailbox to go through?
Hot files
    DECps / Advise (Now C.A. previously VPA)
    Viewpoint (Datametric)
    DLB dynamic load balancer (TTI)

## Slide 8: RMS Tuning
RMS Tuning can be as EASY as
    $set rms/system/indexed/buffer=20
    $set rms/system./extend=2000
    $set rms/system/sequential/buffer=4/block=32
    $set file /global_buffer=20 *.DAT
: … Just Do It!

## Slide 9: RMS Tuning: Just Do It
The 80/20 rule applies
    A little tuning can help a whole lot
    Ideal tuning requires a whole lot
Just get it roughly right and your end-users will love you for it

## Slide 10: Code does not break
Many performance options are transparent
Some require quota / resource adjustment

## Slide 11: Code does not break

## Slide 12: What to look for (Details on next slides)
Bucket Size
Number of Local and Global Buffers
Number of Index Levels (depth)
Duplicate Alternate Key Chains (SIDR)
Allocation and Extend Sizes
Placement in Space and Time
Bucket splits
Compression
Deleted key ranges

## Slide 13: What is a Bucket anyway?
Unit of transfer to IO device
      NOT directly dependent on CLUSTERSIZE
      FINE Tuning with clustersize helps
Contains Data or Index records
      Records can NOT cross bucket boundaries
      If records do not fit, a BUCKETSPLIT occurs
Different sizes for different usage in file
      Data / Level-1 Index / Rest-of-Index / Alternate keys
      RMS memory buffers size = largest bucket size in file
Bucket Size is a Permanent file attribute

## Slide 14: Bucket Size Cheat Sheet

## Slide 15: Bucket Size Cheat Sheet

## Slide 16: What about buffers
A buffer is a chunk of RMS maintained memory to read a bucket (or to write from)
PUTs and UPDATEs need many buffers if multiple keys are in use
Sequential GETs need only 1 buffer
Keyed GETs need 1 for each index level plus one for data (and perhaps for RRV)

## Slide 17: What about LOCAL buffers?
RMS was frugal : just 2 buffers! ( pre 5.4) now ‘deepest index + 2’ is the default
Set on CONNECT time (HLL OPEN call)
Defaults can be set for at process and system level through $SET RMS /BUF…
    but they apply to every file opened!
Local buffer max = 254 through RAB
Specify up to 32K buffers through XABitm

## Slide 18: What about GLOBAL Buffers?
GLOBAL BUFFERS REALLY WORK
Share buffers by all accessors on a node
Efficient in clusters (no change broadcasts)
Expect to SAVE Memory.
    Sure, they use memory, but with many concurrent users they often save memory by requiring fewer local buffers per user ( 100 is less than 30 times 6)
Great to cache (all) index buckets
    Primary and Alternate indexes alike
GLOBAL BUFFERS REALLY WORK

## Slide 19: What about GLOBAL Buffers
Great for read AND write accessed files
    PUTs first need to read where to write.
    Can write from global cache, avoiding next read
Gotchas:
    Up to VMS 7.2 (patch kit for 7.1) a per node serial sequential scan was used to locate buckets under protection of an exclusive, local, lock.
        SHOW PROC/RMS=GBHSH (VMS 7.2+)
    Needs LOCKs to work, thus needs shared access
    ‘Deferred Write’ option forces a local buffer copy
    Not used for DCL opened (process permanent) files
    Sequential readers may trash cache (bad citizens)

## Slide 20: How many GLOBAL Buffers
‘None’ is the only wrong answer.
RMS Limit is 32K, Practical 200 - 2000 ?
42? One for each user?
Cache (top of) index and then some?
Goal is 80 - 99% hit rate.
    But really the goal is an acceptable IO rate.
Treat as memory budget
    You have xxxx pages in the bank to start with.
    spent pages wisely, don’t spend all in one place.

## Slide 21: Duplicate Chains (= SIDR Arrays)
RMS maintains duplicates in arrival order
New inserts must find end of chain potentially requiring many IOs
Problems often seen on SHORT alt. keys
    Increase bucket size to hold average chain
      7 bytes per duplicate on alternate key for flag + RRV
    Apply NULL KEY VALUE (no index entry)
    Add (ordered) key segment to ‘de-duplicate’
    Consider removing the key and sorting as needed
SIDR tool on VMS Freeware CD

## Slide 22: Duplicate Chains (picture)
SIDR Index (=root)
“done”,”*”
Prologue
Key 2
Alternate
Sidr Bucket
Active[1,2] Done[1,2,3]
Sidr Bucket
Done[6,7,8,9,10…99]
Sidr Bucket
Done[100,101,…190]
Sidr Bucket
Done[…] Reques[1,2,3]
No more Index Entry !
RRV’s pointing to User Data Record.
Sidr Data (100/bucket)
Key | Sidrs | Buckets
Active | 2 | 1
Done | 200+ | 4
Request | 3 | 1

## Slide 23: Index Depth
Each level to traverse may need an IO
Each level requires a (temporary) LOCK
Locking ‘amplified’ with global buffers
Bucket locking is cluster wide
Binary search minimizes lock duration
‘Flat’ files are often best but may cause too much contentions. Compensate extra levels through more buffers

## Slide 24: Index Depth Cheat sheet 100,001 records / recordsize =100 / keysize =10 / overhead included

## Slide 25: Index Depth Excel spread sheet
Click on spreadsheet to activate

## Slide 26: Adequate Extends
High price if done wrong
    Not acceptable to run out of disk space while in production
    Frequent file system (XQP) requests each requiring several IOs (worse with High Water Marking)
    Fragmentation
      One bucket requiring multiple clusters = SPLIT IO
      Unwarranted disk head movements
Very easy to do right
    Rely primarily on adequate allocation
    If file needs to grow, allow significant growth
      Gotcha: Maximum extend is 65536

## Slide 27: Compression
DATA and KEY compression is goodness
Save SPACE and save CPU TIME
    Fewer data buckets => fewer IO
    Fewer index keys => fewer index levels
    More effective caches
    Less memory to walk
Remember to verify effectiveness
    FDL has no smarts to detect negative compression
Index compression often discouraged as it prohibits binary searches in index buckets

## Slide 28: Deleted key ranges
Deleted records are purged from the data bucket.
    Space can be re-used for records with similar keys.
    deleted ‘ID’ remains gone, allowing alternate key, and RFA, access to conclude the record was deleted.
    With ‘Fast Delete’ a future alternate key access will remove the associated alternate key.
    Exception: The last key is never deleted, but left
The Primary key index is never removed.
    Buckets remain ‘reserved’ for key range from index.
    CONVERT/RECLAIM designed to clean up (off-line!)
PROBLEM: ‘GET First Record’ may travers empty buckets

## Slide 29: Deleted key ranges (Continued)
Example: “work queue” file with date & time key.
    If work needs to be done, a record is inserted.
    Worker process takes action and deletes record.
    At end of day, no records are left.
If worker falls behind, new records fill up bucket and ‘spill’ into next bucket. The first bucket wil never be re-used for data, because keys increase.
Maximum bucket size (63) may cache queue longer, adding fewer buckets. (watch out for RMS AIJ)

## Slide 30: Deleted key ranges (picture)
Index (=root)
00105, 00912, 02518, *
Prologue
Key 0
Primary
Xab$b_rvb
Xab$b_dvb
Xab$b_lvl = 1
Data (empty)
00085(del)
Data (empty)
00912(del)
Data (empty)
02518(del)
Data (busy!)
04025,04026

## Slide 31: What about IO
Eliminate it: Caches & Application design
A files place in space and time is critical
    Just because it fits, does not make it the right place.
Spread it out
    Multiple disks per application
    Hardware or software striping
    Bound volume sets (area placement)
      Yes, you can bind a Solid State disk with a real disk
    Shadow sets (notably for read intensive)

## Slide 32: What about IO
Speed it up
    Solid state disks (DECram, EZnn)
    Faster disks (10,000 rpm now available)
    Shorter seeks by reducing area on disk
    Faster area on zoned disks
      RZ29 has 16 zones from 67 to 135 sectors per track.
      Some 50% of the data lives in 30% of the seek range
    Track read ahead caching
    Writeback caching (notably with battery backup)

## Slide 33: Bucket Splits
Necessary evil… CONVERT regularly
    RMS keeps records in primary key order
    RMS maintains single pointer from original record file address (RFA) to actual location after split
Cause by random inserts or updates changing the effective record size
Try to add records in primary key order
Fill factor used to avoid or ease splits
    leave room for a few records per bucket
    Localized multiple inserts? Split will make room.

## Slide 34: Cluster size
Fine-tuning. Exercise in trading speed for space.
More important with underlying STRIPING
  EDIT/FDL makes buckets too large for large cluster.
  Make CHUNK, CLUSTER and BUCKET SIZE all have nice factors, notably for small chunks (swxcr).
      Chunk=16, Cluster=64 Bucket=8, NOT bucket = 17
  Each AREA = XQP Extend. Will be cluster aligned
  Buckets will not cross into extends
      By default the data buckets in the first AREA 0 extend are unaligned following the file PROLOGUE. Can be fixed by using area 0 for top index, area 1 for data.

## Slide 35: Assorted Nice to Knows
Convert starts duplicate chains in their own buckets, mostly goodness but…
Use normal editor for FDL files
EDIT/FDL/NOINTER takes TWO inputs:
  File design: Defines keys and such. Do not touch.
  Statistics: really only uses 3 inputs!
    Record count: Set to anticipated value
    average record size: Keep from old stats
    cluster size: Set to small ‘nice’ value: 12? 6?

## Slide 36: Assorted Nice to Knows
Use ANALYZE/SYSTEM to peak at global buffers and hit & miss counters if no file stats.
    SDA> SHOW PROC/RMS=(GBH,GBDSUM)
Tune system files
    sysuaf, rightslist, mail_profile, mail.mai files,...

## Slide 37: Assorted Nice to Knows
Use ‘idle’ program to maintain global buffers when files are not always open. Keep them warm
    Drive with file of files
    Consider touching ‘desirable’ records on startup
    Optionally add check index levels/allocations
Use SHR=NIL to avoid locking
$GET for first record walks index. Cache its RFA in application?

## Slide 38: Assorted Nice to Knows
Records are stored in order by Primary key.
    Assume record has name and number as keys
    If frequent sequential or ‘generic’ search by name is needed and only random access by number then, contrary to popular believe, name should be primary
If significant portion of the file is read by alternate key order, then it will often be more efficient to walk entire file by primary
    With random distribution, each alternate key need an IO to find right data bucket. By contrast, each primary bucket read will return several records

## Slide 39: Patching up broken broken files
The remainder of this presentation was the main contents presented at CETS200

## Slide 40: Anatomy of an Indexed File
Areas
Prologue
Key 0
Primary
Key 1
Alternate
2
1
0
Root
6 *
Index
2 6
Index
*
Data
1 2
Data
3 6
Data
7
Root
Smith *
Index
Jones Smith
SIDR
Bell Jones
SID
Sla..
Down
Down key
Down
Down index
Next
Down
Next
Next
ANALYZE/RMS/INT

## Slide 41: Bucket header $libr/extr=$BKTdef sys$library:lib.mlb

## Slide 42: Record header (Variable, Compression) $libr/extr=$IRCdef sys$library:lib.mlb

## Slide 43: Excuses for corruption
Hardware failure: Disk, controller, cable.
Partial IO due to Power-failure
stop/id (amplified with deferred write usage)
Software failure
  RMS: NO known problems since 6.0
  Experimental defrag tool?
  Privileged code (write logical block)
  Stupid code: $READ/$WRITE indexed files.
  Experimental data caching tool?

## Slide 44: Basic PATCH strategy
Use tools to locate problem zone
Goal is to be able to CONVERT the file
Concentrate on DATA buckets only
Concentrate on bringing bulk of file back
    Trade-off between TIME and DATA
Worry about touching up remainder later.
    Use BACKUPs and application reports to reconstruct any lost records if needed.

## Slide 45: Basic PATCH Analysis tools
ANALYZE/RMS/INTERACTIVE
    Drill down structure as per first slide.
DUMP
    /BLOCK=(START:x, COUNT:y)
    /RECORD=(START:x, COUNT:y)
SEARCH, DIFF, EDT
    Quick tests for linear read.
DCL: READ/KEY
    Quick test for random access read

## Slide 46: Basic PATCHing tools
COPY / BACKUP : Work on test file first!
PATCH… on VAX in cluster.
    ‘vested’ Alpha version is floating around
DCL on file in SEQUENTIAL-512 bytes mode
Reading (CONVERT) by alternate key
ZAP
COPY_BLOCK
‘binary’ file editor ‘rms-edt?’
CONVERT… when all is well again.

## Slide 47: DCL as PATCHing tool
Flip file from indexed to sequential (and back later) in order to read /write a block at a time.
    set file/att=(org=seq,rfm=fix,mrs=512,lrl=512)
    set file/att=(org=idx,rfm=var,mrs=x,lrl=y)
DCL File and symbol manipulations:
    open/read/write file filename.dat
    key[0,32]=vbn_number !Binary key value
    read/key=&key file record
      Use & to postpone symbol substitution, quotes are a problem
    record[x*8,y*8]=z
      replace y bytes at offset x by value z
    write/update/symbol file record
    close file

## Slide 48: ZAP as PATCHing tool
Simple Macro tool to read, update, format, write buckets.
Take your time to study outputs. ‘dense’, but all you need is there.
Uses DBG as GUI
    Define dbg$decw$display “ “
    bucket buffer pointed to by ‘buf’ and R2
    DBG> examin/octaword @r2
    DBG> deposit/byte @r2=0
    DBG> go … back to prompt, format and write.
Click on icon to get source

## Slide 49: COPY_BLOCK as PATCHing tool
Simple C tool to move a block/bucket between files.
May need to update source to your liking (input VBN).
Can be used to ‘clone’ a good (but old) bucket from a backup over a broken file bucket.
Adjust checkbytes… if you are so lucky
Click on icon to get source

## Slide 50: Basic PATCH strategies
Adjust check byte
  Loose nothing?!
Patch ‘around’ broken bucket(s)
  Loose a bucket of records
Adjust next free byte value
  Loose a end portion of bucket
Construct deleted record over bad blocks
  Loose a middle portion of bucket
reconstruct bucket header
  Loose nothing?
‘easy’
‘hard’

## Slide 51: Basic Check byte correction
If somehow the beginning of an updated bucket was written, but not the end, you may only have to make the check-bytes match
Needed for most other steps.
Really easy to do.
Easiest to adjust byte-0 to match last one
  (even though last one is really the bad one)
Done! ‘if you would only be so lucky’

## Slide 52: Patch ‘around’ broken bucket(s)
If the bucket, or a series of buckets really ‘looks like a mess’ (DUMP), then maybe just give up on that data.
Fairly easy to do: Quick & dirty
Set next-vbn in bucket before bad zone to point to first valid bucket after bad zone.
hope that buckets are adjacent.
Verify prior and next bucket VBN with pointers from the index bucket above it.

## Slide 53: Adjust next free byte value
The beginning of an updated bucket was written, but not the end. The free byte points into the end. The new data abruptly flows into old data blocks.
Fairly easy patch.
‘Eye-ball’ dump to find good/back boundary.
ANAL/INT/RMS
  POSITION/BUCKET broken-vbn
  NEXT 9999: run into broken record
  BACK : find start of last good record
  Calculate end of last good record.

## Slide 54: Construct deleted record over bad blocks
Experts only. A lot of work.
Easy to get RMS to loop if done wrong
Fake all but FLAG (deleted) and SIZE
Fake KEY with data key compression (Tricky!)
Maximum data recovery chance!

## Slide 55: reconstruct bucket header
If somehow the beginning of a bucket was overwritten (zeroed out? Text file?)
Al lot of the header data is ‘redundant’
    first check from last
    Since we are only interested in the data level make level=0, and area=0
    vbn sample from vbn address
    flags = 0 (not last bucket is it?)
    next bucket from index (or adjacent value)
Construct deleted record to span into good zone.